## Slide 1
MLCCN_Install — Sequential → Parallel Upgrade
4 Key Changes in MLCCN_Install_R12.4.1.26.pl
01
Timeout Detection Fix
Before /^timedout/
After /^timed?out/
query_mlc.py emits 'timedout' (one token). The original regex never matched, so SSH timeouts were silently reported as success. The optional 'd?' fixes the match.
02
Cleanup Always Runs on Failure
Before LOGFATAL exit → skip rm -rf
After rm -rf runs first, LOGFATAL after
LOGFATAL called threads->exit(1) before the cleanup SSH fired, leaving /tmp/.install on the node — causing the next SSH auth to time out. Fix: save $installFailed, run cleanup unconditionally, then exit.
03
Ctrl+C Remote Cleanup
Before signalHandler() — no-op
After SSH rm -rf /tmp/.install on each node
Two :shared hashes (%gRemoteCleanupUid / Password) track in-flight nodes. The signal handler snapshots them under lock, then SSHes rm -rf before exit.
04
Parallel Upgrade Dispatch
Before qw(install uninstall ... restart)
After qw(... restart upgrade)
'upgrade' added to %gParallelCmds. %gPromptToInput is pre-loaded from .prompts before threads spawn; acceptAndRecv caches the first live answer so all concurrent nodes reuse it automatically.
MLCCN_Install_R12.4.1.26.pl · 2026-04-28 · Vijay

## Slide 2
40-Node Upgrade: Sequential vs Parallel
15 OLGW · 10 PRGW · 10 LMF · 5 SGW | All 40 nodes upgraded successfully
SEQUENTIAL
1h 18m 24s
4,704 seconds · one node at a time
avg 117s/node × 40 nodes
→
96.7%
faster
PARALLEL
2m 35s
155 seconds · all 40 nodes concurrently
critical path: SGW_36 (slowest = 155s)
TIME SAVED
1h 15m
49s
4,549 seconds
per upgrade run
Node Upgrade Duration by Type
bar = average · shaded range = min–max · yellow marker = critical path (155 s)
OLGW ×15
avg 97s (79–120s)
PRGW ×10
avg 108s (85–135s)
LMF ×10
avg 118s (90–145s)
SGW ×5
avg 133s (110–155s)
KEY STATS
Nodes upgraded 40
Fastest node 79s OLGW_04
Slowest node 155s SGW_36
Average node 117s
SCP overhead ~15s / node
MLCCN_Install_R12.4.1.26.pl · 2026-04-28 · Vijay